## Slide 1
Lecture 5
Emergency Response Strategy for Plants
LTP: 3-0-0, CRD: 3
CH 42010: PROCESS PLANT OPERATION & SAFETY

## Slide 2
INTRODUCTION TO EMERGENCY SITUATIONS
Types of emergencies that can arise in industrial settings: Fires, Explosions, Chemical spills, Gas leaks, and Power failures
Bhopal Gas Tragedy
Deepwater Horizon Oil Spill
EMERGENCY RESPONSE PLANNING (ERP)
Source: Google Images

## Slide 3
Source: Google Images
ESP
PSV – Pressure Safety Valve
The Last Line of Defence
Dikes or Containment systems: Type of protection layer used to prevent the release of hazardous materials in the event of a spill or leak
EMERGENCY SHUTDOWN PROCEDURES (ESP)
Cooling
Pumping out
Residuals removal
Blinding and opening
Inspection for entering

## Slide 4
Source: Google Images
PSV – Pressure Safety Valve & RV – Relief Valve
Overpressure of a chemical process plant may lead to major hazard (fire, explosion and toxic release)
The 1st line of defense against overpressure hazard is good pressure control: PCV – Controlling the process pressure within safe operating pressure region
The 2nd line of defense against overpressure hazard is to install PSV/RV to relief liquid or gases before excessive pressures are developed
RV | PSV
Primarily for liquid service | Steam, gas & vapor service
RV should open at the set pressure (normally less than 10% of operating P) and reaches full capacity at 25% overpressure. RV closes as the system pressure returns to the set pressure. | PSV should open at the set pressure and reseat after reaching approximately 4% below set P.
EMERGENCY SHUTDOWN PROCEDURES (ESP)

## Slide 5
Source: Google Images
Spring operated PSV/RV which can be used repeatedly:
  Conventional.
  Balanced Bellow: eliminating the back pressure effect when the device activates and avoid direct contact of corrosive media with spring etc.
Rupture Disc: A calibrated sheet of metal designed to rupture at a specified pressure. Can be used one time only.
Guidelines where RVs should be installed:
  All vessels need reliefs, including reactors, storage tanks, towers and drums.
  Blocked-in sections of cool liquid-filled lines which are exposed to heat (e.g., cooling water side of a heat exchanger) or refrigeration need reliefs.
  Positive displacement pumps, compressors and turbines need reliefs on the discharge side.
  Vessel steam jackets are often rated for low pressure steam. Reliefs are installed in jackets to prevent excessive steam pressures due to operator error or pressure regulator failure.
  Storage vessels need pressure and vacuum reliefs to protect against pumping in or out of a blocked-in vessel or against the generation of a vacuum by condensation.
All reliefs devices should be inspected for their functionality and set pressure during shut-down.
EMERGENCY SHUTDOWN PROCEDURES (ESP)
PSV – Pressure Safety Valve & RV – Relief Valve

## Slide 6
FMEA
HAZOP
FTA
Plant-specific emergency procedures and emergency shutdown processes for critical equipment
Importance of proper signage, alarms, and emergency lighting
Evacuation procedures and Communication protocols
Source: Google Images
EMERGENCY RESPONSE PLANNING (ERP)

## Slide 7
Factory Acts & Rules
Boiler Act 1923
State Boiler Rules
Indian Boiler Regulations 1950
The Petroleum Act & Rules
The Explosive Act & Rules
The Insecticide Act & Rules
The Poisonous Acts & Rules
The Electricity Act & Rules
Gas Cylinder Rules 1981
Static & Mobile Pressure Vessels 1981
Water & Air Pollution Control Acts & Rules
Environment Protection Act 1986 & Rules
Hazardous Waste Management Rules 1989
MSIHC Rules 1989
Chemical Accident Rules 1996
Bio Medical Waste Rules 1998
Building & Construction Act 1996.
Radiation protection Rules
Atomic Agency Act
Governmental Rules & Regulations (Govt. of India)
Source: Google Images
EMERGENCY RESPONSE PLANNING (ERP)

## Slide 8
Governmental Rules & Regulations (Govt. of India)
BIS Standards
Source: Google Images
Oil Industry Safety Directorate (OISD) – Ministry of Petroleum and Natural Gas
EMERGENCY RESPONSE PLANNING (ERP)

## Slide 9
Protective Equipments (PPE) - fire-resistant clothing, breathing apparatus, and chemical-resistant gloves.
Level A
Level B
Level C
Level D
Eye and Face Protection: ANSI Z87.1-2010, ANSI Z87.1-2003, or ANSI Z87.1-1989(R1998).
Head Protection: ANSI Z89.1-2009, ANSI Z89.1-2003, or ANSI Z89.1-1997.
Foot Protection: ASTMF-2412-2005 and ASTMF-2413-2005, ANSI Z41-1999, or ANSI Z41-1991.
Electrical Rubber Insulating Equipment: ASTM D120-09, ASTM D-178-01 (2010), ASTM D-1048-12, ASTM D-1049-98 (2010), ASTM D-1050-05 (2011), or ASTM D1051-08.
Occupational Safety and Hazard Administration (OSHA) requires PPE to meet the following ANSI standards
https://www.osha.gov/sites/default/files/publications/osha3151.pdf
Source: Google Images
American National Standards Institute (ANSI)
PERSONAL SAFETY

## Slide 10
Source: Google Images
Sulfuric Acid (Conc.)
Methanol
PERSONAL SAFETY

## Slide 11
Source: Google Images
PERSONAL SAFETY

## Slide 12
Stages of Fire
Fire Tetrahedron
Source: Google Images
FIRE SAFETY

## Slide 13
The Temperature of Fire
Source: Google Images
FIRE SAFETY

## Slide 14
CAUSES OF FIRE IN A CHEMICAL PLANT
Source: Google Images
FIRE SAFETY AND PREVENTION

## Slide 15
Source: Google Images
Remember this acronym when using an extinguisher – P. A. S. S.
FIRE SAFETY AND PREVENTION

## Slide 16
Source: Google Images
FIRE SAFETY AND PREVENTION

## Slide 17
Pool Fire
Liquid spills onto the ground forming a pool. The volatile liquid (example: petrol) evaporates into atmosphere to form flammable mixture, ignited and form pool fire. The heat vaporizes more fuel and air is drawn in round to the side to support combustion. Danger to people is by direct thermal radiation.
Flash Fire
Relatively volatile spilled material (example: propane, butane, LPG) forms a pool with rapid evaporation forming sizeable vapor cloud, drifted away by wind, ignited by ignition source to form flash fire. People is at risk from thermal radiation effect.
Torch Fire
High pressure release of gas from a pressure vessel or pipeline ignites almost immediately, forming torch fire with flame length tens of meters. Danger arises from thermal radiation and also impingement on adjacent pressurized vessel containing liquefied petroleum gas (LPG) may cause vessel failure from boiling liquid expansion vapor explosion (BLEVE).
Source: Google Images
FIRE SAFETY AND PREVENTION

## Slide 18
Source: Google Images
Explosion is sudden and violent release of energy physically or chemically. Examples of chemical explosion are explosion from explosive material and exothermic chemical reaction.
Examples of physical explosion are explosion due to fracture of a vessel containing high pressure gas or steam due to over pressure.
In general, explosion can be divided into two types:
  Deflagration: resulting shock wave moving at the speed less than speed of sound (Mach Number < 1).
  Detonation: resulting shock wave moving at the speed greater than speed of sound (Mach Number > 1), i.e., shock wave followed closely by a combustion wave.
FIRE SAFETY AND PREVENTION
Source: Google Images

## Slide 19
Unconfined Vapor Cloud Explosion (UVCE)
It is an explosion due to the ignition of large pre-mixed cloud of flammable vapor and air of concentration within the flammable range.
Popular example:
Flixborough, 1974 in which a major leak of hydrocarbon occurred at a reactor non-standard modified piping, forming vapor cloud, ignited and led to UVCE.
Confined Vapor Cloud Explosion (CVCE)
Vapor explosion occurs within a vessel or building.
Popular example: Abbeystead disaster, 1984, in which methane gas in water pumping station ignited killing several visitors.
Boiling Liquid Expanding Vapor Explosion (BLEVE)
Vessel containing flammable liquid (e.g., LPG) is heated by fire from neighbouring vessel. The flammable liquid vaporized and build pressure, vessel weakened and finally ruptures creating vapor cloud and explodes. Casualties are from blast effect, thermal radiation or missiles.
Popular example: Feyzin 1966 involving propane tank and San Juanico, Mexico City 1984 involving LPG tank.
Dust Explosion (DE)
Results from the rapid combustion of fine combustible solid particles (dust in grain silo, iron & aluminum dust).
Popular example: New Orleans in 1977 in which 45 silos containing corn, wheat and soy beans were involved.
FIRE SAFETY AND PREVENTION

## Slide 20
EMERGENCY EVACUATION
Emergency evacuation is the urgent immediate egress or escape of people away from an area that contains an imminent threat, an ongoing threat or a hazard to lives or property.
In situations involving hazardous materials or possible contamination, evacuees may be decontaminated prior to being transported out of the contaminated area.
Evacuation Sequence:
  Detection
  Decision
  Alarm
  Reaction
  Movement to an area of refuge or an assembly station
  Transportation
The time for the first four phases is usually called pre-movement time.
The most common equipment to facilitate emergency evacuations are fire alarms, exit signs, and emergency lights. Some structures need special emergency exits or fire escapes to ensure the availability of alternative escape paths.
Source: Google Images
EVACUATION PROCEDURES

## Slide 21
Source: Google Images
RCA
POST-EMERGENCY PROCEDURES & INCIDENT INVESTIGATION